## Slide 1
iFAMS Deconvolution Software for Mass Spectrometry Analysis
James S. Prell
Department of Chemistry and Biochemistry
University of Oregon, Eugene, OR

## Slide 2
What Can We Study with iFAMS?
(interactive Fourier-Transform Analysis for Mass Spectrometry)
Native protein complexes:
  Stoichiometry and oligomer state profiles, dependence on conditions
Membrane protein complexes:
  Lipid or other ligand binding—how many, which molecules?
Antibodies, glycosylated and modified proteins:
  Quantitation from intact ion mass spectra

## Slide 3
Polydispersity and heterogeneity: the dreaded “blob” spectrum
MSP1D1 Nanodisc
with POPC lipids
10000
12000
14000
16000
m/z
0
20
40
60
80
100
abundance (arb. u.)
m/z
Staph A.
α-hemolysin
pores in
FOS-14 detergent
micelles
Polydisperse non-covalent and/or covalent adducts
give rise to “frequencies” in extremely congested mass spectra
that allow us to analyze them much more easily in the frequency domain.
Synapt G2-Si
Orbitrap EMR

## Slide 4
Fourier Transform analysis for polydisperse Nanodiscs
mass spectrum
Fourier spectrum
Fourier duality:
“ugly” mass spectra often yield clean Fourier spectra
m/z
“frequency”, z/(Δm)
Synapt G2-Si

## Slide 5
mass spectrum
Fourier spectrum
m/z
“frequency”, z/(Δm)
Fourier peak spacing = 1/lipid mass,
now charge states can be easily (automatically!) assigned
measured lipid mass: 734.1 ± 0.2 u
(DPPC mol. wt. 734.0 u)
Fourier Transform analysis for polydisperse Nanodiscs

## Slide 6
mass spectrum
Fourier spectrum
m/z
“frequency”, z/(Δm)
inverse Fourier transform of Fourier peaks
yields charge-state-specific mass spectral envelopes
(stoichiometry profile)
IFT
Fourier Transform analysis for polydisperse Nanodiscs

## Slide 7
Quiz Time!
Suppose iFAMS identifies fundamental peaks for you at frequencies
0.02802, 0.02950, 0.03097, and 0.03245 (= z/subunit mass)
What is the subunit mass?
What are the charge states?
~678 Da
19, 20, 21, 22+
At what frequency would you find the 3rd harmonic
peak for the 20+ charge state?
0.08850

## Slide 8
Stoichiometry characterization of “large” Nanodiscs
lipid stoichiometry ↓
as lipid footprint ↑
charge state
Cleary, Prell and co., J. Am. Soc. Mass Spectrom. 2018, 29, 2067

## Slide 9
PEGylated Protein Analysis
input identical
raw nESI
mass spectra
1+ MALDI-TOF
data
Campuzano et al. Anal. Chem. 2019, 91, 9472-9480
Sample: PEGylated Granulocyte Colony Stimulating Factor
(PEG-GCSF)

## Slide 10
Gábor Transform: localized frequencies
1. multiply mass spectrum by Gaussian (or other shape) window
2. find FT frequencies within windowed spectrum
3. slide window to the right
4. repeat, and plot FT spectra vs. window center (2D “spectrogram”)
ESI spectrum of
PEG:PPG:PEG
block copolymer
relative abundance
1000
2000
3000
4000
m/z
Cleary and Prell
ChemPhysChem 2019

## Slide 11
Wilson, Prell and co. Anal. Chem. 2019
Chirp patterns make it easy to find complexes of different composition
GT spectrum practically
analyzes itself!
Ions overlapped in both
m/z and frequency
are resolved!
membrane pore toxin α-hemolysin
in detergent micelles
Notes: So we can then analyze these three overlapping distributions and we find our highest frequency distribution corresponds to the detergent micelle embedded heptamers, the middle distribution is actually two distributions with nearly stripped heptameric complexes and micelle embedded hexamers that overlap significantly in m/z and charge state, and our lowest frequency distribution corresponding to the nearly detergent stripped hexameric pore complexes

## Slide 12
Quiz Time!
For a biomolecular ion, why should frequency
decrease left-to-right in mass spectrum?
High charges are on the left for a native ion,
so frequency = z/(subunit mass) will be
higher on the left, at lower m/z.

## Slide 13
iFAMS Can Also Distinguish Types of Compositional Heterogeneity
“simple” mixture:
superposition of “pure” populations
“random” mixture:
convolution of subunit populations
Cleary and Prell Analyst 2020 DOI:10.1039/D0AN00726A

## Slide 14
Mixed-Lipid Nanodisc Composition
See
Cleary and Prell Analyst
2020 DOI:10.1039/D0AN00726A
for mathematical proof of method
and Hoi, Robinson, Marty Anal Chem
2016 DOI: 10.1021/acs.analchem.6b00851
for a nice illustration of same concept

## Slide 15
PEG
PPG
PEG
Block Copolymer Composition
Sigma (manufacturer):
average mass 8400 Da
3.8:1 PEG:PPG units
(1H-NMR headgroup analysis)
iFAMS:
average mass 8370 ± 970 Da
PEG mass 6810 ± 880 Da
PPG mass 1560 ± 420 Da
4.37:1 PEG:PPG
Richer information from iFAMS nESI data
Eliminate contributions from low-mass polymer interferents

## Slide 16
iFAMS Tutorial Demonstration
Download at:
github.com/prellgroup/iFAMS/releases
You’ll want to download and unzip
iFAMS_V5.4_GUI.zip

## Slide 17
iFAMS_V5.4_GUI
is the interactive
version of iFAMS

## Slide 18
We’re going to load up a file called “test.csv” to illustrate a lot of the iFAMS features.
Note that iFAMS will take .csv or .txt files (first column is m/z, second column is abundance)
as input files.
(You can easily export these from just about any commercial MS software.)

## Slide 19
We’re going to load up a file called “test.csv” to illustrate a lot of the iFAMS features.
Note that iFAMS will take .csv or .txt files (first column is m/z, second column is abundance)
as input files.
(You can easily export these from just about any commercial MS software.)

## Slide 20
We’re going to load up a file called “test.csv” to illustrate a lot of the iFAMS features.
Note that iFAMS will take .csv or .txt files (first column is m/z, second column is abundance)
as input files.
(You can easily export these from just about any commercial MS software.)

## Slide 22
The test.csv mass
spectrum is polydisperse
with multiple overlapped
charge states.
Already you can see that the Fourier
spectrum is a lot simpler.

## Slide 23
Zoom tool
fundamentals
harmonics

## Slide 25
Here, we are telling iFAMS where
we want it to look for peaks in the FT
spectrum.

## Slide 26
iFAMS found the charge states
for the fundamentals and the
subunit mass.
Note: 8/6 are multiples of 4/3,
so we expect some harmonic
interferences with FT analysis

## Slide 27
There may be times when you want to tell iFAMS directly what you know the charge states and
subunit mass to be. Just depends on your needs!

## Slide 28
This is the DECONVOLUTION step.

## Slide 30
data from fundamentals alone
harmonic artifacts

## Slide 31
Including more harmonics will improve the resolution of the deconvoluted data.

## Slide 32
Here, we are going to include 4 harmonics.
Generally, include as many as are resolved
in your FT spectrum without extreme
harmonic overlap.

## Slide 33
We now have much better resolution
in the deconvolved spectrum,
…BUT we also have some artifacts
due to harmonics.

## Slide 34
Here’s a zoom of our results.
It is essentially exactly correct.
If you like these results, you can
export them.

## Slide 36
A new folder has been created
with all of your results so far.

## Slide 37
The results are labeled by type:
“ifft” = inverse Fourier transform data
= charge-state-specific mass spectrum;
“zerocharge” = contribution to “zero charge”
mass spectrum
and by charge state (3,4,5,6,7,8+, here)

## Slide 38
But what if you want higher selection capabilities, e.g., to eliminate harmonic artifacts or exclude a
contaminant? Try Gábor Transform (STFT)!

## Slide 39
Sometimes, you can’t see the peaks
in the Gabor spectrogram right away.
need to adjust the color scale!
This is identical to the FT spectrum
from the Fourier Analysis Tool,
just turned sideways, because
frequency is now our y-axis
This is just the raw
mass spectrum, and
it will stay here.
This is where our
GT results will start
to appear as we go.

## Slide 42
There they are! Note that
the upper peaks are
just a reflection of the bottom
peaks (you can ignore them).

## Slide 43
Changing color max
may make peaks
easier to see.

## Slide 44
Let’s also try
changing the
freq resolution.

## Slide 45
Now that we like what we see, we can zoom in to the region of interest (use the magnifying glass!
you can always undo your zoom by pressing the  arrow or go back to the original zoom with the “home” button).

## Slide 46
We are ready to ANALYZE the data. You need to UNCLICK the magnifying glass button first!

## Slide 47
Left-click and drag to draw a box around a fundamental you want to analyze. If you want to modify your box, click
and drag the corners until you are happy with it. Once done, hit Ctrl-E to add it to the developing spectrum.

## Slide 48
If you are ready to move on to the next charge state, hit Ctrl-S to save your work. The box will acquire a thicker border
when you have done this.
Down here, you can
already see your
reconstruction
“developing”.

## Slide 49
Here, I’ve selected and saved each of the
fundamentals. Note how the 3/4+
peaks don’t overlap with 6/8+ at all!

## Slide 50
Now that you have picked your fundamentals,
iFAMS can automatically select harmonics
and add them to the deconvolution.

## Slide 51
Again, let’s use 4 harmonics.

## Slide 53
Once you’ve picked the harmonics,
tell iFAMS the charge states in
the order you selected them.

## Slide 54
Unlike our earlier FT
analysis, GT analysis
has NO harmonic artifacts!
(Recall, that happened because
we are in a deliberately hard
situation with low charge states.)

## Slide 55
Here, I have zoomed in.

## Slide 56
Now, what if you need integrated peak areas and/or heights from your deconvolution?

## Slide 57
Hopefully, these items are self-explanatory.
The “minimum distance between peaks”
simply helps you deal with any remaining
noise, if need be.

## Slide 58
If your list is a lot longer than this, iFAMS will pop out
a scrollable window.

## Slide 59
Again, you can export all of your results so far (charge-state-
specific mass spectra, zero-charge deconvolution, and
integrated peak/peak height list).

## Slide 60
This file contains the integrated
peaks and their centroid masses.

## Slide 61
Real Sample: α-Hemolysin from Staph. aureus
in intact FOS-14 detergent micelles
A couple notes:
We use just the raw mass spectrum with no pre-smoothing or pre-filtering
(not necessary, because GT is itself a “notch” filter by nature)
Going into this, we know:
1) monomer weighs 33,259 Da (from no-detergent measurements)
2) FOS-14 weighs 379.5 Da

## Slide 62
Where is the signal?
Zoom in on the FT spectrum 

## Slide 65
Note how complex FT spectrum is.
GT is easier to “read”!

## Slide 66
Can already see two native ion types!

## Slide 67
I just selected the boxes quickly; you could be more precise if you like.
Get charge states by hovering over middle of box,
read of frequency coordinate, multiply by
known FOS-14 mass. e.g., 0.05797*379.5 = 22+

## Slide 69
Hover cursor over peak to get
mass (or look at output file).
Based on known αHL and FOS-14
monomer masses,
240,745 Da = (αHL)6 + 109 FOS-14
277,360 Da = (αHL)7 + 117 FOS-14
hexamer
heptamer
…and of course we could include harmonics to get lipid resolution

## Slide 70
Thanks for your attention, and happy deconvolution!
github.com/prellgroup/iFAMS/releases